Title:		Drawing No:				Rev
Weld-On Thread Adapter Crush Ring
Machine:		Program No.:
		10061
Material Type (MC number):	Material Size:				Material Bhn:
1045 T&G	2" Diameter x Bar				150Bhn
Workholding Device:			Operation(s):
Three-jaw chuck			2	of			4
Programmer:
Stephane Drouin-Moreland

Workholding Set-up
Work Coordinate Offset: G54	A: 1.0 ± 0.02”	B: 0.1”

Special Instructions:

Operation:	Rough Face and OD
Cutting Head ID:					Insert ID:	ID: CNMG-432 PM 4325
Cutting Unit ID:	C4-DCLNR 27050-12				Clamping Unit ID:	C4-RC2040-51030M
Turret Position	Offset #		Tip Code	TNR (re)	Velocity (Vc)	RPM (n)	Feed Rate (fn)	DOC Range
01	01		3	0.0313	990sfm		0.05-0.0118in/rev
Notes:

Operation:	Finish Face and ODDNMG-331 PF 4325
Cutting Head ID:					Insert ID:	DNMG-331 PF 4325
Cutting Unit ID:	C4-DDJNR-27050-11				Clamping Unit ID:	C4-RC2040-51030M
Turret Position	Offset #		Tip Code	TNR (re)	Velocity (Vc)	RPM (n)	Feed Rate (fn)	DOC Range
02	02		3	0.0156	990sfm		0.0040in/rev
Notes:

Operation:	Drill and ID
Cutting Head ID:					Insert ID:	80-05 03 05H-C-LM 1044, 880-05 03 W08H-P-LM 4044
Cutting Unit ID:	880-D2600C4-03				Clamping Unit ID:	C4-NC3000-V40-03 0
Turret Position	Offset #		Tip Code	TNR (re)	Velocity (Vc)	RPM (n)	Feed Rate (fn)	DOC Range
07	07		2	0.0313	493sfm	1720	0.0045in/rev
Notes:		X-axis offset is centerline, Z-axis offset should be found based on the peripheral inserts.

Operation:	Champher and Part-Off
Cutting Head ID:					Insert ID:	N123G1-0300-0002-CM 2135
Cutting Unit ID:	C4-RF123G20-27060B				Clamping Unit ID:	C4-RC2040-51030M
Turret Position	Offset #		Tip Code	TNR (re)	Velocity (Vc)	RPM (n)	Feed Rate (fn)	DOC Range
09	09		4	0.0079	438		0.004
Notes:		Probe the grooving/part-off tool using the left side of the probe and set it to tip code 4.

Operation:
Cutting Head ID:					Insert ID:
Cutting Unit ID:					Clamping Unit ID:
Turret Position	Offset #		Tip Code	TNR (re)	Velocity (Vc)	RPM (n)	Feed Rate (fn)	DOC Range

Notes:

Operation:
Cutting Head ID:					Insert ID:
Cutting Unit ID:					Clamping Unit ID:
Turret Position	Offset #		Tip Code	TNR (re)	Velocity (Vc)	RPM (n)	Feed Rate (fn)	DOC Range

Notes:

Operation:
Cutting Head ID:					Insert ID:
Cutting Unit ID:					Clamping Unit ID:
Turret Position	Offset #		Tip Code	TNR (re)	Velocity (Vc)	RPM (n)	Feed Rate (fn)	DOC Range

Notes: